W2160

Product Specification

(V1.0)

Beijing Watchdata Co. Ltd.

2018/2

W2160 is a highly integrated USB card reader, it integrates image scanning technology on the traditional smart card reader .It can support  QR code or bar code scanning , and has a contact card slot and support contactless card operation.  The reader also has a magnetic stripe card reading function, and can be equipped with a second-generation ID card information reading function to meet various needs of customers.

### READER FEATURES:

  - Support the contact card that satisfies standard ISO 7816－1/2/3/4

  - Support the contact I2C memory card, SLE4428, SLE4442,AT88SC1608

  - Support 1.8V/3V/5V Card

  - Support the contactless card that satisfies standard ISO14443 TYPEA and TYPEB

  - Support the Magnetic Strip card satisfies standard ISO 7810, ISO 7811,ISO 7812 and ISO 7813

  - Full speed USB communication ,HID protocol

  - LED indicates the power or communication status

  - Embedded buzzer that can be controlled by the user

  - With the DLL, user can operate card conveniently

| Module | Description |
| --- | --- |
| Scanner | 2D:QR code/ PDF417code; 1D: Code 128, Code 93, F-6, ITF-14, EAN-13, MSI- Plessey, Code 39 ,Code 11,etc. |
| Support Card type | Contact card : ID-1 size slot;Support T0, T1 protocol,I2C Memory Card ,SLE4428,SLE4442, AT88SC 1608; Support 1.8V/3V/5V card Contactless card： TYPEA /TYPEB/MAFIRE ONE Read Range of Contactless Card is 0～4.5CM Magnetic strip card: Support the second track and the third track reading PSAM: Support 4 PSAM slots |
| Communication | Full Speed USB Interface with 12Mbps,HID communication Protocol |
| Indication | 3 LEDS & Buzzer; the red led indicates power status, the green led indicates contact card operation status, the blue led indicates contactless card operation status |
| Power Supply | USB power supply |
| MTBF | 5000 hours |
| Working Current | ≤500mA |
| Dimension | 127*79*65(mm) |
| Temperature | 0℃ ～ 50℃ |
| Humidity | 20% ～ 90% |
| Shell Material | ABS |
| Operation system | Win XP/ Vista/ Win 7/Win 8/ Win 10/linux/ |